# Requirements:
## 1) Object recognition

Requirement:
The system must be able to autonomously identify desired objects.

Rationale:
To enable the system to differentiate between desired and undesired objects.

Objective:
Must(s)	Should(s)	Could(s)
Recognise a single object at a single orientation from a distance of 2m	Recognise a single object at multiple orientations from a distance greater than 2m	Recognise multiple objects; differentiate between two similar objects

Test Scheme:
Success rate;

Must(s)	Should(s)	Could(s)
70% true positive, 10% false positive in a single structured environment	Do better	Do better

Risk to the project if not complete:
5

## 2) General object location

Requirement:
The system must be able to determine the location of a desired object.

Rationale:
This is needed to provide a goal location for the mobile platform to bring the gripper with reach of the object.

Objective:
Must(s)	Should(s)	Could(s)
Provide location of object within a 1m radius	Provide location of object within 30cm radius	Provide location of object within 10cm radius

Test Scheme:
Reliability

Must(s)	Should(s)	Could(s)
20% success rate	50% success rate	70% success rate

Risk to the project if not complete:
5

## 3) Navigating to object

Requirement:
The system must be able to position itself such that the end effector can be guided to a desired object

Rationale:
To pick up the desired object needs to be within the arms operating range
Objective:
Must(s)	Should(s)	Could(s)
Position the gripper within operating range with 10% success rate	Position the gripper within operating range with 50% success rate	Position the gripper within operating range with 90% success rate

Test Scheme:
Reliability
Must(s)	Should(s)	Could(s)
Have gripper within range of object after 10 attempts; 10% success rate	Have gripper in range after two attempts 50% success rate	Have gripper in range first attempt

Risk to the project if not complete:
5

## 4) Gripper positioning

Requirement:
The system must be able to guide a grasping mechanism to a desired object

Rationale:
To lift the object the gripper must be positioned within gripping range

Objective:
Must(s)	Should(s)	Could(s)
within 8cm radius	within 5cm radius	within 2cm radius

Test Scheme:
Must(s)	Should(s)	Could(s)
30% success rate	50%	70% success rate

Risk to the project if not complete:
3

## 5) Kinematic model of arm

Requirements text:
The system must have a mechanism capable of grasping a variety of objects.

Rationale:
In order to transport the object the system must be able to pick it up.

Objective:
Must(s)	Should(s)	Could(s)
Minimum of two objects from a single orientation	Minimum of two objects from multiple orientations	More than two objects from multiple orientations

Test Scheme:
Measure success rate of grasping an object with enough grip to lift the object.
Must(s)	Should(s)	Could(s)
30% success rate from a single orientation	50% success rate from two orientations	70% success rate from four orientations

Risk to the project if not complete:
5

## 6) Location storage

Requirements:
The system must be capable storing the location of identified objects

Rationale:
In order for the system to be able to fetch an object, the system must be able to store a general location of the object

Objective:
Must(s)	Should(s)	Could(s)
Store xy coordinate of platform when object is identified	Store xy coordinate of object relative to base and xy coordinate of platform when object is identified	Store xy coordinate of object relative to map

Test Scheme:
Does the system successfully store locations
Must(s)	Should(s)	Could(s)
Succeed	N/A	N/A

Risk to the project if not complete:
2

## 7) User interface

Requirements:
The system must have a user interface operable by untrained personnel.
Rationale:

Objective:
Must(s)	Should(s)	Could(s)
Some form of user interface	Intuitive GUI	Voice control

Test Scheme:
Can the user readily see;
Must(s)	Should(s)	Could(s)
Untrained user can operate with strict instruction	Untrained user can operate with limited instruction	Untrained user can operate with zero instruction

Risk to the project if not complete:
1