Systems overview:

The system will comprise of the following key hardware systems:
Base:
Most of the work for the self-localising base was completed as part of Toms 3rd year project. The key components of the base are:
- Chassis
- Motors/driver
- LIDAR
- Laptop
- Batteries (power supply)
- Encoders
For more information on the base of the robot (including functionality and work done), please look here: https://github.com/carebare47/dalek/blob/master/Autonomous%20Dalek%20Project%20Report.docx

Arm:
The arm we will be using was designed by Martin Stoelen. We will be borrowing it for the duration of the project. The arm uses co-contracting agonist-antagonist pairs of motors to vary the stiffness over several key joints allowing the compliance over these joints to be set.

Gripper:
The gripper will be primarily build from 3D printed parts and eight servos. The gripper will have four ‘fingers’, the design of which is inspired by the fin-ray effect gripper. A paper describing the original fin-ray gripper can be found here: https://www.frontiersin.org/articles/10.3389/frobt.2016.00070/full

Cameras:
The robot will use at least two cameras. The first (hand camera), mounted in the gripper, will be used for precise grasping of the object. The second camera (head camera) will be mounted on the highest point of the robot and will serve to identify and store the locations of objects.

Base sensors:
The base of the robot is equipped with two incrimental wheel encoders and a 2D LIDAR. The encoders are used to limit the velocity of the wheels to prevent the robot moving faster than the SLAM system is able to keep track of.

The system will comprise of the following key software systems:

Navigation:
The majority of the navigation system has already been developed. More information on this can be found in the git repository linked above.

Arm:
The arm has a kinematic model/solver, but does not come with high-level control algorithms. A node will be written to generate end-effector goals for the arm from both camera systems.

Gripper:
A control program will be developed to provide an abstracted interface to control of the grippers servos. Control inputs to this program will include the triggering of sequences of poses and control over individual servo angles. This program will also generate control signals for the LED ring array around the hand camera.

Gripper camera:
This program will process fiducials seen by the hand camera and generate signals instructing the arm to align the gripper with the object to be grasped. The program will also trigger the gripper closing when it in position.

Head camera:
The software for the head camera will detect objects as the robot drives around and send their locations to the waypoint node to be saved. In addition, the head camera program will be used to point the hand camera at the object we wish to pick up.

Waypoint node:
The waypoint node will serve as the universal goal coordinate saving and loading system. The robot base can currently save its current location as a waypoint. If the robot moves somewhere else and this waypoint is loaded as a goal for the navigation system, the robot will return to where it was when the waypoint was saved. This node will have the following inputs and outputs:
Node inputs:
- Should it save a waypoint?
- Should it be where I am or somewhere else?
- With respect to which coordinate frame should it save the waypoint?
- What should it label the waypoint?
- Should it load a waypoint?
- Which waypoint should it load?

The output of this node will be goals published for the navigation system to head towards.